## Slide 1: Ohm's law and resistors
V = I R
Voltage across a resistor = current x resistance

## Slide 2: Series circuits
Same current through every resistor
Voltages add up
R_eq = R1 + R2 + R3

## Slide 3: Parallel circuits
Same voltage across every branch
Currents add up
1/R_eq = 1/R1 + 1/R2 + 1/R3

## Slide 4: Ideal voltmeter
Infinite resistance: no current flows through it
Acts like an open circuit, NOT a wire
Connected in parallel; reads the potential difference between its two points
Notes: Trap: a resistor in series with an ideal voltmeter has no current, so no voltage drop.

## Slide 5: Ideal ammeter
Zero resistance: acts like a wire
Connected in series with the component

## Slide 6: Kirchhoff's current law
At a junction: current in = current out
Charge cannot accumulate at a node

## Slide 7: Current division
In parallel, I_k = I_total x (1/R_k) / sum(1/R)
Smaller resistance takes more current